## Slide 1: DB_FRA_Analysis_GUI
Uses an improved test for significant responses based on confidence interval assuming a Poisson distribution around mean spontaneous firing rate
Centroid at each sound level is calculated from significant responses and is called the best frequency.
  Response at lowest stimulus level (ie, minimum threshold) is called the characteristic frequency.
Bandwidths calculated for each sound level around best frequencies as twice the standard deviation.
Receptive field borders also estimated (manually adjustable) at each sound level above minimum threshold.
Rate-Level Curve analysis based on ± octaves around best frequencies
  Rate-level curve is normalized using D’
  Monotonicity index is computed from normalized rate-level curve
    Monotonic response = 0.0
    Non-Monotonic response < 0.0
Methods Reference: Escabi et al, Neuroscience 150 (2007) 970-983
Stolzberg 2014

## Slide 2
Control Window
Rate-Level Curve and Monotonicity Index
FRA Analysis Results
FRA Temporal Response
GUIs

## Slide 3
Use DB_Browser to locate unit for analysis
Add “DB_FRA_Analysis_GUI” to “Analysis Tools”
  Click “Settings” -> “Analysis Tools”
  Click “Add Tool”
  Enter “DB_FRA_Analysis_GUI” (without quotes)
  Select protocol from “Available” list and click “Add >>”
  Click “Done”
  The block may need to be reselected in DB_Browser
  DB_FRA_Analysis_GUI should be available in the drop-down list in Analysis Tools

## Slide 4
0.0 < value < 1.0
Window to compute mean firing rate
relative to stimulus onset.
Must have 2 values.
Distribution of spontaneous firing rates (black bars)
Distribution of FRA firing rates (cyan line)
Click to update unit_properties table on database with analysis results (including any manual adjustments)
Click to update unit_properties table on database indicating displayed unit is not good. No other values are updated.
Control Window
Recompute FRA analysis based on confidence level and analysis window.
Note: any manual adjustments will be discarded.

## Slide 5
FRA analysis
FRA is computed by taking mean firing rate over analysis window (set in control window) and smoothing using a Savitzky-Golay filter over both dimensions.
Clicking on FRA plot will adjust minimum threshold and recompute features
  Note: minimum threshold can only be adjusted to a higher level
Bandwidth = 2∙σ
±
Best Frequency (centriod)
white-filled is characteristic frequency/minimum threshold
Adjustable frequency bandwidth range

## Slide 6
Temporal response map
Plots slice of FRA map at one sound level against time
Clicking on FRA plot will adjust high or low frequency borders
Procedure:
  Data is binned at each frequency
  Bins are divided by bin size (1 ms) and number of stimulus repetitions to compute mean firing rate
  Mean firing rate map is smoothed with a 2 dimensional gaussian kernel (5 freq x 10 ms) and rescaled
Select intensity level to display
Stimulus onset
Same measures as FRA plot

## Slide 7
Manually adjusting receptive field borders
Clicking temporal response will adjust both this plot and FRA plot
Automated analysis
Manually adjusted analysis

## Slide 8
Normalized with D’
Mean firing rate ±standard error of the mean
Rate-Level Curve
Rate-level curve computed from ±octaves around best frequency (centroid) at each sound level
D’ is computed to normalize the RLC for comparison across different firing rates
Monotonicity index is computed from D’ RLC as the minimum observed D’ at sound levels higher than the maximum firing rate level